## Slide 1: Using Simulink for Model-Based Simulations
Timothy Kyung
UC Irvine
05/25/2023

## Slide 2: We need to shift verification left
Source: Clive Maxfield and Kuhoo Goyal “EDA: Where Electronics Begins”
Where errors are introduced (yellow) vs. detected (blue)

## Slide 3: Why is developing complex systems expensive?
Source: Return on Investment for Independent Verification & Validation, NASA, 2004.
Cost to Correct Defect
Phase Detected
Phase Introduced
Concept
Requirements
Design
Implementation
Test
Test
Implementation
Design
Requirements
Concept
Cost
Notes: https://www.nasa.gov/centers/ivv/pdf/398308main_Value%20Report%20Final.pdf

## Slide 4: Traditional Development
Requirements and specifications
Design and implementation
Mechanical components
Embedded software
Requirements are captured in text and may be ambiguous
Physical prototyping is expensive!
  Subsystems are often developed independently
  Code is often hand-written
  Problems are undiscovered or discovered late, when they are costly to fix.
Electrical Components
EDA
INTEGRATION AND TEST
SPECIFICATIONS
Mechanical Components
MCAD/ MCAE
DESIGN AND IMPLEMENTATION
Control Algorithms
Control
Design
Embedded Software
C/C++
REQUIREMENTS
RESEARCH
Notes: This is a natural way to solve an engineering problem. First research and state requirements, then we have a meeting to make sure that we’re all on the same page. We break the huddle, separate into teams, and each team builds its subsystem. Then we combine the subsystems in a prototype and test it.
But there are some problems with this plan.
It’s difficult for engineers to compare their design to the specifications because they are not integrated with the design process. The model and requirements are disconnected, so it can be challenging to recognize whether the current design still satisfies the requirements.
Since the teams are more or less siloed and much of the testing happens near the end of the process, there are many opportunities for defects to appear. Prototypes are costly. Using domain-specific modeling environments precludes system-level simulations, so these tests have to wait until the prototyping stage.

## Slide 5: Ariane
~2X payload
Ariane 5 design and test

## Slide 6: Ariane
Notes: The crash, triggered by the ground crew, was attributed to an overflow. The controls software on Ariane 5 was recycled from the smaller Ariane 4. Its rocket motor actuators had a larger range of motion. Physical signal inputs, no longer constrained to the bounds that applied to the smaller rocket, caused an overflow on the controller.
The Ariane 5 inherited requirements from its predecessor. The design process followed the path: Requirements -> Model -> Test/Integrate/Build. Finally, long after modeling and testing, a change was made to the hardware. Had this change been evaluated in a model that also served as an executable set of requirements, this failure mode may have been found before flight.
MBD allows modeling of not just the physical system, but also logic (like the controls algorithm) and fixed-point behavior.

## Slide 7: Ariane
Notes: The failure resulted in a loss of more than US$370 million.

## Slide 8: Shifting Left with Model-Based Design
Model-Based Design is a problem-solving method that treats the model as the single source of truth.
The model
  is an executable requirements document.
  lets us simulate many domains in one environment.
  enables early, continuous testing.
  serves as a source for code generation.
INTEGRATION
IMPLEMENTATION
Embedded software
and digital electronics
DESIGN
System-level and
component-level models
RESEARCH
REQUIREMENTS
TEST AND VERIFICATION
Notes: Show quadcopter demo, explain how Simulink facilitates model-based design

## Slide 9: Model-Based Design Enables Iteration
Test
Evaluate
Change design, requirements
To what degree does my problem-solving framework allow me to model, predict and improve?
Feynman problem-solving algorithm:
Write down the problem.
Think very hard.
Write down the answer.
Notes: It’s rare that the first design is the best one. Design is normally an iterative process. Engineers come up with a design, implement it, and then test it. The results of these test then need to be evaluated before a new design change is made.

## Slide 10: Phoenix Mars Lander: A Model-Based Design Success Story
Notes: Phoenix was a robotic spacecraft on a space exploration mission on Mars under the Mars Scout Program. The Phoenix lander landed on Mars on May 25, 2008. Mission scientists used instruments aboard the lander to search for environments suitable for microbial life on Mars, and to research the history of water there. The total mission cost was about US $386 million, which includes cost of the launch.

## Slide 11: Phoenix
“This multi-body simulation provided sufficient confidence … to alleviate concerns.”
“Simulations using the high-fidelity radar model revealed that … the radar may report wildly incorrect altitudes.”
From Under the Radar: Trials and Tribulations of Landing on Mars.
Locked on ground
Locked on heat shield

## Slide 12: Where can you find hardware support packages?
https://www.mathworks.com/hardware-support/home.html

## Slide 13: Working with Hardware Support Packages in Simulink
Device Driver Blocks
Algorithm Under Test

## Slide 14: Generate Production Ready Code from Key Algorithms

## Slide 15: Integrating Generated Code with Hand Code Example: Arduino IDE Integration with Generated Code
Call Model_Init() Once at Initialization
Call Model_Step() every 2.77mS
#include generated .h files

## Slide 16: Integrating Generated Code with Hand Code Example: NXP S32 Design Studio IDE Integration with Generated Code
#include generated .c & .h files
Call Model_Step() in loop

## Slide 17: Benefits of Prototyping on Evaluation Boards with Simulink
Kickoff your hardware+ software integration on Day-1
Focus on key algorithm design
Shorten design iterations due to code generation
Evaluate performance of your algorithms on final target hardware

## Slide 18: How does MATLAB fit into model-based design?
Technical computing & data analysis are an important part of the design process
Simulink is built on top of MATLAB
  Use the right tool for the job
Technical Computing Workflow

## Slide 19: MathWorks Support Mechanisms: Collaboration Ensures Success
Application Engineering
Pilot Engineering
Training
Consulting
Technical Support
Product questions
General support
Product/Capability demonstrations
Lunch-&-Learns, Workshops, WebEx’s, etc.
Evaluation support
Complimentary, guided support for adoption of new tools/processes
Deep engagement evaluations/ demonstrations
Paid training on specific tools and/or processes
On-site, web-based instructor lead, & self-paced online
Paid engagements (custom targets, tool customization, advisory services)
508-647-7000